## Slide 1: Introduction to OpenLane
Presented by
Hafiz Wajeh ul Hasan
Workshop Session 2

## Slide 2: Contents
OpenLane
PDK
Foundry
Prerequisites for an ASIC Design
Sky130 PDK
LAB PRACTICE

## Slide 3: OpenLane
What is OpenLane?
  OpenLane is an automated RTL to GDSII flow
  The flow performs full ASIC implementation steps from RTL all the way down to GDSII
  Amalgamation of open-source Electronic design automation (EDA) Tools

## Slide 4
Synthesis
Floorplan/Power Network
Placement
CTS
Routing
RC Extraction
GDS Generation
Physical Verification
Yosys, OpenSTA
init_fp, ioplacer, pdn
RePLace,OpenDP
TritonCTS
FastRoute, TritonRoute
SPEF-Extractor
Magic
Magic
Open-source EDA Tools
Input
Input
Input
Input
Input
Input
Input
Input
Output
Output
Output
Output
Output
Output
Output
Design.v, Design.sdc, Std_cells.lef, Std_cells.lib
Design_gate_level_netlist.v
Design_gate_level_netlist.v, macro.lef, macro.cfg
Floorplan.def
Floorplan.def
Placement.def
Design_gate_level_netlist.v, Placement.def
CTS.def, CTS_netlist.v
CTS.def
Routing.def
Routing.def
Design.spef
Routing.def
Design.gds, Design.lef
Design.gds
Input
Output
APR Step
EDA Tool
OpenLane

## Slide 5: OpenLane Flow
The inputs of the flow?
  Design.v/RTL
  PDK
What is a PDK?

## Slide 6: PDK (Process Design Kit)
It's a set of libraries and associated data to design in a particular technology
Simpler terms- A PDK contains:
  Transistors
  Standard Cells (for digital design)
  Design Rules
  Timing/Power Information etc. in library file
  Layer information
D
S
G
Feature Size
Technology
  130nm
  90nm
  65nm
  45nm
  30nm
Feature Size

## Slide 7: Foundry
Who provides the PDK?
  FOUNDRY!
What is a Foundry?
  It is a factory where devices such as ICs are manufactured
Foundry
You
PDK
GDS
ICs
Designing
Fabrication
Completed
Completed
Foundry
You

## Slide 8: Prerequisites for an ASIC Design
3 key ingredients
  RTL/Design
  EDA Tools
  PDK
RTL
RTL
EDA TOOLS
EDA TOOLS
PDK
PDK
ASIC DESIGN
RTL – You can write on your own
EDA TOOLS – You can find open-source tools
PDK - ??????
Until June 2020, the open-source community did not have any solution for accessing PDK!

## Slide 9: Sky130 PDK
First ever open-source PDK
Multiple process libraries
  High speed
  High density etc.
Contains Standard cells operated at 1.8V
1 level of local interconnect, 5 levels of metal

## Slide 10: LAB PRACTICE